## Slide 1: GraspVLA Inner Workings
Goal: explain how GraspVLA works to the benchmark team
Scope: public release plus what we have already run on em14

## Slide 2: Why This Paper Matters
Synthetic-data pretraining for grasping instead of large real robot logs
Direct end-to-end baseline for our benchmark against modular systems
Public release focuses on deployment: server, simulation, and real-world controller

## Slide 3: Public Release Pieces
GraspVLA repo: model server and offline test
GraspVLA-playground repo: validation, playground, and LIBERO evaluation
GraspVLA-real-world-controller repo: Franka plus dual-camera client
Full training stack and SynGrasp-1B are not fully public

## Slide 4: Server API
Inputs: front_view_image, side_view_image, proprio_array, text
Prompt wrapper: In: What action should the robot take to {instruction}?
ZeroMQ service returns action deltas plus debug bbox and pose
serve.py warms up the model before opening the request loop

## Slide 5: How The Model Produces A Grasp
Token pattern: text_ids, bbox, hist_proprio, cur_proprio, goal, eos
Autoregressive stage predicts bbox and goal tokens
Flow matching stage generates continuous action trajectory
Output is detokenized back to xyz, rpy, and gripper

## Slide 6: Important Code Paths
prompt.py for the CoT prompt wrapper
token_pattern.py for bbox and goal token layout
model/vla/__init__.py for autoregressive plus flow-matching generation
model/vla/flow_matching.py for the action head
scripts/serve.py for deployment inference

## Slide 7: Current Lab Status
Official model server is running on em14:6666
Official validate_server.py and offline_test.py both succeeded on em14
Official playground.py and evaluate_libero_tasks.py now run in gb-graspvla-sim
Official complete sim batch is done: playground 8/10, libero_object 482/500, libero_10 325/350, libero_goal 336/350
The 350 denominators are expected: libero_10 exposes 7 tasks and libero_goal skips 3 invalid tasks
GraspVLA smoke success 1/1 at about 377 ms
Contact-GraspNet smoke success 1/1 at about 405.6 s
AnyGrasp is blocked only by license, not by repo setup

## Slide 8: Next Step For The Team
Use the complete official GraspVLA sim run as the anchor reference
Run a small Track A batch with GraspVLA and Contact-GraspNet
Fetch the AnyGrasp license and complete the third baseline
Collect plots, failure taxonomy, and videos for the benchmark meeting